## Slide 1: Cs 207 Project
LASER SECURITY SYSTEM

## Slide 2: Arduino and Breadboard

## Slide 3: First, connect Arduino with breadboard
5 Volts with (+)
Ground with (-)

## Slide 4
Connecting on the other side of breadboard
5 Volts with (+)
Ground with (-)

## Slide 5: Red led
Connect pin 13 to positive leg of led.(use resistor in between pin 13 and + leg)
Connect (-) side of led to ground.

## Slide 6: Blue led
Connect pin 12 to positive leg of led.(use resistor in between pin 12 and + leg)
Connect (-) side of led to ground.

## Slide 7: photoresistor
Connect (+) leg of photoresistor to 5v
Connect ground and A0 of photoresistor to –ve leg.
You can use resistor on either side.

## Slide 8: buzzer
Connect (+) leg of buzzer in pin 9
Connect ( - ) leg of buzzer to ground.

## Slide 9: Fingerprint sensor
There are 4 wires in fingerprint sensor.
Red – connect in (+) 5v
Black – connect to ( - ) ground
White – Connect to pin 3
Yellow - Connect to pin 2

## Slide 10: Servo
There are 3 wires connecting to Arduino
Red – connected to (+) 5v.
Brown – connected to ( - ) ground
Yellow – Connected to pin 11.

## Slide 11: Laser light
We have connected laser light using another Arduino. But you can use in same Arduino to give power.
Connect one end to 5 Volts
Connect other end Ground